## Slide 1: INGI2145: CLOUD COMPUTING (Fall 2014)
Cloud Networks
12 December 2014
Certain lecture slides adapted judiciously from Duke CPS590 by T. Benson and Cornell CS5413 by H. Weatherspoon

## Slide 2: Today
Modern data centers need modern networking!
FatTree-based DC fabric
Software-Defined Networking

## Slide 3: Datacenter!
10s to 100s of thousands of servers
Clusters of homogeneous servers
  10s of racks with 10s of serves in each rack
  Each server: many cores, memory, network interfaces, local storage (HDD and/or SDD)
Individual requests may be served by 10s to even 1000s of serves
  Performance based on slowest response
  Network congestion affects performance
  Overprovisioning large-scale networks is too costly

## Slide 4: Networking in Data Centers
Internet
Core Switch (CS)
Aggregate Switch (AS)
Top of Rack (ToR)
Bisection bandwidth

## Slide 5: Goals of Data Center Networks
Support diverse application
  High throughput/low latency
  Utilize multiple paths
Scale to cloud size
  Support large number of addresses
  5-10 million VMs
Support flexible resource utilization
  Support seamless VM mobility

## Slide 6: Goals of Data Center Networks
Uniform high capacity:
  Maximum rate of server to server traffic flow should be limited only by capacity on network cards
  Assigning servers to service should be independent of network topology
Performance isolation:
  Traffic of one service should not be affected by traffic of other services
Layer-2 semantics:
  Easily assign any server to any service
  Configure server with whatever IP address the service expects
  VM keeps the same IP address even after migration

## Slide 7: Common data center topology
Internet
Servers
Layer-2 switch
Access
Data Center
Layer-2/3 switch
Aggregation
Layer-3 router
Core

## Slide 8: Problem with traditional DC topology
Single point of failure
Over subscript of links higher up in the topology
  Trade off between cost and provisioning

## Slide 9: Problem with traditional DC topology
Oversubscription:
  Ratio of the worst-case achievable aggregate bandwidth among the end hosts to the total bisection bandwidth of a particular communication topology
  Lower the total cost of the design
  Typical designs: factor of 2:5:1 (400 Mbps) to 8:1 (125 Mbps)
Cost:
  Edge: $7,000 for each 48-port GigE switch
  Aggregation and core: $700,000 for 128-port 10GigE switches
  Cabling costs are not considered!

## Slide 10: Properties of desired solutions
Backwards compatible with existing infrastructure
  No changes in application
  Support of layer 2 (Ethernet)
Cost effective
  Low power consumption & heat emission
  Cheap infrastructure
Allows host communication at line speed

## Slide 11: Backwards compatibility tradeoffs
Specialized hardware and communication protocols, such as InfiniBand, Myrinet
  Can scale to clusters of 1000s of nodes with high bandwidth
  Expensive infrastructure, incompatible with TCP/IP applications
Leverage commodity Ethernet switches and routers to interconnect cluster machines
  Backwards compatible with existing infrastructures, low-cost
  Aggregate cluster bandwidth scales poorly with cluster size, and achieving the highest levels of bandwidth incurs non-linear cost increase with cluster size

## Slide 12: Facebook Example
Introduction to Facebook's data center fabric

## Slide 13: Today
Modern data centers need modern networking!
FatTree-based DC fabric
Software-Defined Networking

## Slide 14: FatTree based solution
Adopt a special instance of a Clos topology
Similar trends in telephone switches led to designing a topology with high bandwidth by interconnecting smaller commodity switches

## Slide 15: FatTree based solution
Connect servers using a fat tree topology
  K-ary fat tree: 3-layer topology (edge, aggregation and core)
    each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
    each edge switch connects to k/2 servers & k/2 aggr. switches
    each aggr. switch connects to k/2 edge & k/2 core switches
    (k/2)2 core switches: each connects to k pods
Edge
Aggregation
Core
Pod

## Slide 16: FatTree based solution
Why Fat Tree?
  Fat tree has identical bandwidth at any bisections
  Each layer has the same aggregated bandwidth
Built out of cheap devices with uniform capacity
  Each port supports same speed as server
  All devices can transmit at line speed if packets are distributed uniform along available paths
Great scalability
  A k-port fat tree supports k3/4 servers

## Slide 17: Problems with a vanilla Fat Tree
Layer 3 will only use one of the existing equal cost paths
  Bottlenecks up and down the fat-tree
Packet re-ordering occurs if layer 3 blindly takes advantage of path diversity
  Further load may not necessarily be well-balanced
Wiring complexity in large networks
  Packing and placement technique

## Slide 18: FatTree modified
Enforce a special (IP) addressing scheme in DC
  Allows host attached to same switch to route only through switch
  Allows inter-pod traffic to stay within pod
  unused.PodNumber.switchnumber.Endhost

## Slide 19: FatTree modified
Use two level look-ups to distribute traffic and maintain packet ordering
First level is prefix lookup
  used to route down the topology to servers
Second level is a suffix lookup
  used to route up towards core
  maintain packet ordering by using same ports for same server
  diffuses and spreads out traffic

## Slide 20: Optimization: Flow classification
Denote a flow as a sequence of packets
pod switches forward subsequent packets of the same flow to same outgoing port
And periodically reassign a minimal number of output ports
Eliminates local congestion
Assign traffic to ports on a per-flow basis instead of a per-host basis
  Ensure fair distribution on flows

## Slide 21: Optimization: Flow scheduling
Pay attention to routing large flows, edge switches detect any outgoing flow whose size grows above a predefined threshold, and then send notification to a central scheduler
The central scheduler tries to assign non-conflicting paths for these large flows
Eliminates global congestion
Prevent long lived flows from sharing same links
Assign long lived flows to different links

## Slide 22: Fault Tolerance
Each switch in the network maintains a BFD (Bidirectional Forwarding Detection) session with each of its neighbors to determine when a link or neighboring switch fails
Failure between upper layer and core switches
  Outgoing inter-pod traffic, local routing table marks the affected link as unavailable and chooses another core switch
  Incoming inter-pod traffic, core switch broadcasts a tag to upper switches directly connected signifying its inability to carry traffic to that entire pod, then upper switches avoid that core switch when assigning flows destined to that pod

## Slide 23: Fault Tolerance
Failure between lower and upper layer switches
  Outgoing inter- and intra pod traffic from lower-layer,
    the local flow classifier sets the cost to infinity and does not assign it any new flows, chooses another upper layer switch
  Intra-pod traffic using upper layer switch as intermediary
    Switch broadcasts a tag notifying all lower level switches, these would check when assigning new flows and avoid it
  Inter-pod traffic coming into upper layer switch
    Tag to all its core switches signifying its ability to carry traffic, core switches mirror this tag to all upper layer switches, then upper switches avoid affected core switch when assigning new flows

## Slide 24: Evaluation
Benchmark suite of communication mappings to evaluate the performance of the 4-port fat-tree using the TwoLevelTable switches, FlowClassifier ans the FlowScheduler and compare to hierarchical tree with 3.6:1 oversubscription ratio

## Slide 25: Results: Network Utilization

## Slide 26: Results: Heat & Power Consumption

## Slide 27: Perspective
Bandwidth is the scalability bottleneck in large scale clusters
Existing solutions are expensive and limit cluster size
Fat-tree topology with scalable routing and backward compatibility with TCP/IP and Ethernet
Large number of commodity switches have the potential of displacing high end switches in DC the same way clusters of commodity PCs have displaced supercomputers for high end computing environments

## Slide 28: Other Data Center Architectures
A Scalable, Commodity Data Center Network Architecture
  a new Fat-tree “inter-connection” structure (topology) to increases “bi-section” bandwidth
  needs “new” addressing, forwarding/routing
VL2: A Scalable and Flexible Data Center Network
  consolidate layer-2/layer-3 into a “virtual layer 2”
  separating “naming” and “addressing”, also deal with dynamic load-balancing issues
Other Approaches:
  PortLand: A Scalable Fault-Tolerant Layer 2 Data Center Network Fabric
  BCube: A High-Performance, Server-centric Network Architecture for Modular Data Centers

## Slide 29: Today
Modern data centers need modern networking!
FatTree-based DC fabric
Software-Defined Networking

## Slide 30: Classical network architecture
Distributed control plane
Distributed protocols compute routing state
  OSPF, IS-IS, BGP, etc.
Specialized Packet Forwarding Hardware
Feature
Feature
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 31: Network Policies
Access control: reachability
  Alice can not send packets to Bob
Application classification
  Place video traffic in the gold queue

## Slide 32: Network Management: Past

## Slide 33: Networking Yesterday
Data plane
  Determines how to forward a packet
  Looks up the forwarding table to determine output port for a packet
Control plane
  Determines how to populate the forwarding tables
  Translate user commands into hardware
    ACLs, MPLS
  Runs a bunch of routing protocols
    IGPs: OSPF, IS-IS, RIP, & EGPs: BGP
OSPF
MPLS
IP
BGP
VLAN
10.10.2.10
1
2.3.4.23
3
Prefix
Port
23
1
45
3
MPLS Label
Path

## Slide 34: Networking Yesterday
Control + Data-plane on each device
  Network is a Distributed systems
  Built to avoid failure (ArpaNet)
A network is supported by an infinite number of protocols
  New protocols developed to support new functionality
  Takes time to standardize and to change the hardware
Think: writing a distributed program in Perl
  Error prone (Over 50% of errors caused by misconfig)
  Time consuming
    IT Operators are the most costly portion of IT
    Takes up to 6 months for ISPs to roll out services for new costumers
    Very difficult to add new functionality into the network
Notes: Perl analogy  need for a higher level abstraction for doing things

## Slide 35: Separation of control and data planes
Specialized Packet Forwarding Hardware
Feature
Feature
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Specialized Control Plane
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 36: Requirements for SDN
Operate without Guarantees
  Need abstraction for distributed state
  Want to deal with information without worrying about the fact that the state is from a distribution
  Logically Centralized
Compute configuration of each device
  Need abstraction that simplifies configuration
  Want to specify your intent  desired goal; the what
  NOT: how to do it.
Operate within given network-level protocol
  Need abstraction for forwarding model
  Hide details about hardware specifics
  No need to worry about he exact hardware
OpenFlow Protocol
Network Operating
System
Network Operating
System

## Slide 37: Enter Software Defined Networking: Separation of concerns
Network operator
  Specify behavior on a model
  Behavior == network policies
Network runtime
  Provides abstract view of the network
  Maps abstract view to global view
  Function of the types of network policies to be supported
Network Operating System
  Maps global view to physical view
  Translate abstract commands to device configuration
  Device interface: forwarding abstractions

## Slide 38: Software Defined Networking (SDN)
Global Network View
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Network OS
Constructs a logical map of the network
OpenFlow
Open vendor-agnostic protocol
Simple packet forwarding hardware
Feature
Feature

## Slide 39: Software Defined Networking (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Network OS
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
Constructs a logical map of the network
OpenFlow
Open vendor-agnostic protocol
Simple packet forwarding hardware

## Slide 40: Software Defined Networking (SDN)
Global Network View
Network Virtualization
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Abstract Network View
Control
Programs
Control
Programs
Control
Programs
firewall.c
…
if( pkt->tcp->dport == 22)
dropPacket(pkt);
…
Packet
Forwarding
Network OS
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…

## Slide 41: What problem does SDN solve?
Great tool to enable innovation in network control
Platform to help solve longstanding problems in managing networks and deploying new functionality

## Slide 42: SDN applications
Network management
  Enterprise access, middleboxes waypointing
Monitoring and measurement
Network virtualization
User mobility and VM migration
Server load balancing
Traffic engineering
  Energy efficiency, high WAN utilization
Exposing an API to host applications

## Slide 43: OpenFlow
is a protocol for remotely controlling the forwarding table of a switch or router
is one element of SDN

## Slide 44: OpenFlow Protocol
Message between controller and switches
  Synchronous
    Stats, Flow-mods
  Asynchronous
    Packet-in
Abstract hardware details
Allows direct control over forwarding table
10.2.3.4:10.2.3.3
Fwd Port 1
A2:e3:f1:ba:ea:23:*
Drop
Match
Action

## Slide 45: How does OpenFlow work?
Ethernet Switch

## Slide 46
Data Plane (Hardware)
OpenFlow Agent
OpenFlow Controller
OpenFlow Protocol (SSL/TCP)

## Slide 47: Main components of an OpenFlow switch
Controller
Hardware
Layer
Software
Layer
Flow Table
OpenFlow Agent
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
Flow Table
…
pipeline
Group Table
OpenFlow protocol
Meter Table

## Slide 48: Flow Table Entries
Match fields | To match against packets. These consist of the ingress port and packet headers
Priority | Matching precedence of the flow entry
Counters | e.g. packet and byte counters
Instructions | Determine action set or pipeline processing
Timeouts | Maximum amount of time or idle time before flow is expired by the switch
Cookies | Opaque data value chosen by the controller. Not used when processing packets.
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
The match field contains either a specific value or a “wildcard”
VLAN
pcp
IP
ToS
Main components of a flow entry in a flow table.

## Slide 49: Match/action examples
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:20..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
22
drop

## Slide 50: Examples
Routing
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
vlan1
*
*
*
*
*
port6,
port7,
port9
00:1f..

## Slide 51: Headers as a protocol-agnostic collection of bits
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace

## Slide 52: “Flowspace”: A way to think about flows defined by match fields
IP SA
IP DA
Single flow
All flows from A
A
All flows between two subnets

## Slide 53: Flowspace: Generalization
Field 2
Field 1
Single flow
Set of flows
Field n

## Slide 54: OpenFlow key messages
Message | Direction | Description
Packet-In | Switch->Controller | Transfer the control of a packet to the controller. Packet-in events can be configured to buffer packets
Packet-Out | Controller->Switch | Instruct switch to send a packet out of a specified port. Send in response to Packet-in messages.
Modify-State | Controller->Switch | Add, delete and modify flow/group entries in the flow tables and to set switch port properties
Flow-Removed | Switch->Controller | Inform the controller about the removal of a flow entry from a flow table

## Slide 55: Further readings
A Guided Tour Through Datacenter Networking Abts, D., Felderman, B. Communications of the ACM(CACM), 55(6), 2012http://queue.acm.org/detail.cfm?id=2208919
The next-generation Facebook data center network http://bit.ly/1xp8fbi
A scalable, commodity data center network architecture Al-Fares, M., Loukissas, A., & Vahdat, A. SIGCOMM 2008
OpenFlow: Enabling Innovation in Campus Networks McKeown, N., Anderson, … Turner, J. ACM SIGCOMM Computer Communication Review, 38(2), 2008
Software-Defined Networking at the Crossroads S. Shenker https://www.youtube.com/watch?v=WabdXYzCAOU

## Slide 56: Numbers Everyone Should Know
Source: http://i.imgur.com/k0t1e.png
Numbers by Jeff Dean (Google)

## Slide 57: That’s all
Hope you enjoyed INGI2145!
Exam: 17 January 8:30 – BARB 91